GUIDE SPECIFICATIONS

INTERIOR –  VERTICAL OR HORIZONTAL CLADDINGS

PRODUCT: WOOD WALL SYSTEM

Division 10 - Specialties

Section 10.000 –Vertical or horizontal Cladding

1.0 	GENERAL

1.1	RELATED SECTIONS:

1.1.1	Section		0…..

1.1.2	Section

1.1.3	Section		0…..

Products supplied by this section and installed by other trades:

Specifier co-ordinate this work with designated trades in other sections of these project specifications.

    - Fabricated Wood Vertical or Horizontal cladding installed to the wall as indicated on the architectural drawings.

    - Steel or aluminum attachment brackets for fixed vertical or horizontal cladding

1.2	SUMMARY:

1.2.1	Provide Interior fixed wood vertical or horizontal cladding with related specified hardware to complete the installation to the following locations:

Specifier provide the scope of the work

    - Vertical or Horizontal cladding shall be mounted to brackets/ stringers/trims protruding from the wall /  façade as indicated on the architectural drawings

    - Wood cladding supplied and installed by other trades shall be coordinated with this trade to ensure smooth integration of the specified system

  - QUALITY ASSURANCE:

    - All bidders submitting bids on the work of this section shall meet or exceed the quality of materials, components and assemblies herein. Bidders who do not comply with these specifications shall refrain from submitting a bid

    - Alternate bids, alternate products shall be submitted to the Design Consultant ten (10) days prior to tender closing. Alternate bids can only be submitted as an alternate to the specified base bid product

    - Manufacturer shall have a minimum of five (5) years experience in the manufacture of the specified shading system. All work specified under this section shall be supplied by one subcontractor

    - Conform to applicable Building Codes, relevant local codes and all other standards noted

Specifier provide details of any specific codes to be met

    - Install one complete sample with accessories on site. Review the installation before proceeding with the remainder of the work. Adjust sample installation, as required, to gain acceptance. Accepted work may form part of the final installation

  - SUBMITTALS AND TEST REPORTS:

    - Submit fully detailed drawings prepared in AutoCAD 2000 version format showing all components, finishes and other construction conditions, installation, controls and all applicable dimensions according to Section 01300 – Submittals

    - Submit duplicate samples of the key components of the specified fixed horizontal or vertical cladding with the specified finish. Minimum size 40” (1000mm) for review

    - Submit duplicate samples of the specified brackets and attachment methods

    - Submit duplicate copies of maintenance instructions including the name, address and other contact details of local service company

  - INSPECTION / PREPARATION

    - Verify that the structure necessary to carry the vertical or horizontal cladding is a proper installation and secure

    - Notify general contractor in writing of any deficiencies in the work of other trades that would affect the fixed horizontal or vertical cladding.

    - Make accurate measurements at the site before fabrication. Check layout of glazing framing sections, spans and loading capabilities

  - DELIVERY, STORAGE AND HANDLING:

    - Do not deliver to site until areas to receive the fixed horizontal or vertical cladding are completely finished.

    - Deliver materials in original protective wrappers or containers, with manufacturer’s labels and sealed intact.

    - Handle and store materials in accordance with the manufacturer’s recommendations, protecting materials and finishes from damage or soiling.

  - WARRANTY:

    - Provide a limited manufacturer’s warranty from date of Substantial Completion covering the following periods:

Wood wall system			One (1) year

1.7.2	Provide a limited installation warranty from date of Installation of one (1) year

- PRODUCTS

2.1 MANUFACTURER:

2.1.1	Hunter Douglas Architectural Products

5015 Oakbrook Parkway, Suite 100

Norcross, GA 30093

United States

Tel: 	800-366-4327

Fax: 	770-806-0214

Web:	www.hunterdouglascontract.com

2.2 MATERIALS:

2.2.1	Wood wall:

Specifier: Dependent upon the system selected above, certain items in the section will need to be deleted

Mounting profiles and clips:

Specifier select appropriate option

- System to be attached to mounting profiles and clips to be supplied by the manufacturer of the fixed vertical or  horizontal cladding. Brackets to fix to:

Specifier select the appropriate option

  - Projecting studs supplied by the wall manufacturer

  - Nosing of the window wall mullions

  - Brick or block work, using resin anchors or similar

  - Studs (provided by the structural steel contractor) projecting through the cladding

  - Steel work behind the cladding using engineered steel or aluminum spacers to take up the distance between the steel structure and the cladding,

Wood wall:

System shall incorporate:

- Flat surface formed by agglomerated wood Fire Resistant (class A) veneered in both faces whit a total thickness of 16mm

- The wood wall system module is:

Wide: 290mm; 299mm; 595mm or 604mm.

Length: 1200mm; 1800mm or 2400mm.

- The wood  wall system shall comprise the following components:

  - Aluminum Beam profile

  - Aluminum Corner profile

  - Upper clip

  - Lower clip

    - Material quality and finishes:

  - Finishes can be perforated, unperforated or grooved.

- Veneer Alternatives:

Specifier select finish from current selections, please proceed to: http://www.hunterdouglascontract.com/ceilings/woodwright/naturaplanktile/index.jsp

- EXECUTION

3.1   FABRICATION:

3.1.1	System components manufactured and assembled allowing for custom installation techniques to suit project requirements

3.1.2	Finished assemblies shall be square, true to size and free from twist or other defects that could affect their strength or appearance. Factory applied finish should be uniform, smooth and without blemishes

3.2   INSTALLATION:

3.2.1	Install work using skilled tradesman and install in strict accordance with manufacturer’s recommendations.

3.2.2	All items installed, plumbed, squared and rigidly anchored maintaining uniform clearances and accurate alignment measurements

3.2.3	The fixed horizontal or vertical cladding shall be pre-measured and manufactured off-site.

  - ADJUSTING AND CLEANING:

3.3.1	Adjust components as required to ensure trouble free performance

3.3.2	Prior to Substantial Completion clean down once the fixed horizontal or vertical cladding.

3.3.3	Replace work which cannot be satisfactorily repaired, adjusted or cleaned.

END