GUIDE SPECIFICATIONS

INTERIOR CEILING – NATURA WOOD CEILING

Division 10 - Specialties

Section 10.000 –CEILINGS

1.0 	GENERAL

1.1	RELATED SECTIONS:

1.1.1	Section		0…..

1.1.2	Section

1.1.3	Section		0…..

Products supplied by this section and installed by other trades:

Specifier co-ordinate this work with designated trades in other sections of these project specifications.

    - Fabricated WOOD CEILING installed to the ceiling l as indicated on the architectural drawings.

    - Steel or aluminum attachment profiles for fixed horizontal ceilings

1.2	SUMMARY:

1.2.1	Provide Interior wood ceiling with related specified hardware to complete the installation to the following locations:

Specifier provide the scope of the work

    - Horizontal wall ceiling shall be mounted to “T” profiles to hang from the concrete /  Steel structure ceiling as indicated on the architectural drawings

    - Wood ceiling supplied and installed by other trades shall be coordinated with this trade to ensure smooth integration of the specified system

  - QUALITY ASSURANCE:

    - All bidders submitting bids on the work of this section shall meet or exceed the quality of materials, components and assemblies herein. Bidders who do not comply with these specifications shall refrain from submitting a bid

    - Alternate bids, alternate products shall be submitted to the Design Consultant ten (10) days prior to tender closing. Alternate bids can only be submitted as an alternate to the specified base bid product

    - Manufacturer shall have a minimum of fifteen (15) years experience in the manufacture of the specified shading system. All work specified under this section shall be supplied by one subcontractor

    - Conform to applicable Building Codes, relevant local codes and all other standards noted

Specifier provide details of any specific codes to be met

    - Install one complete sample with accessories on site. Review the installation before proceeding with the remainder of the work. Adjust sample installation, as required, to gain acceptance. Accepted work may form part of the final installation

  - SUBMITTALS AND TEST REPORTS:

    - Submit fully detailed drawings prepared in AutoCAD 2000 version format showing all components, finishes and other construction conditions, installation, controls and all applicable dimensions according to Section 01300 – Submittals

    - Submit structural calculations for local approval, taking account of maximum potential wind  loads

    - Submit duplicate samples of the key components of the specified  horizontal wood ceiling with the specified finish. Minimum size 24” (600mm) for review

    - Submit duplicate samples of the specified brackets and attachment methods

    - Submit duplicate copies of maintenance instructions including the name, address and other contact details of local service company

  - INSPECTION / PREPARATION

    - Verify that the structure necessary to carry the horizontal wood ceiling is a proper installation and secure

    - Notify general contractor in writing of any deficiencies in the work of other trades that would affect the horizontal wood ceiling

    - Make accurate measurements at the site before fabrication.

  - DELIVERY, STORAGE AND HANDLING:

    - Do not deliver to site until areas to receive the horizontal wood ceiling are completely finished

    - Deliver materials in original protective wrappers or containers, with manufacturer’s labels and sealed intact

    - Handle and store materials in accordance with the manufacturer’s recommendations, protecting materials and finishes from damage or soiling

  - WARRANTY:

    - Provide a limited manufacturer’s warranty from date of Substantial Completion covering the following periods:

Wood ceilings:	One (1) year

1.7.2	Provide a limited installation warranty from date of Installation of one (1) year

- PRODUCTS

2.1 MANUFACTURER:

2.1.1	Hunter Douglas Architectural Products

5015 Oakbrook Parkway, Suite 100

Norcross, GA 30093

United States

Tel: 	800-366-4327

Fax: 	770-806-0214

Web:	www.hunterdouglascontract.com

2.2 MATERIALS:

2.2.1	Wood ceiling:

Specifier: Dependent upon the system selected above, certain items in the section will need to be deleted

Suspension system:

Specifier select appropriate option

- The wood ceiling installs on a 15/16” T-Grid system, whose main profile is  1 ½” (38mm) of height and a width of 15/16” (24mm), and

- The system is complemented with 2 antiseismic clips fabricated in galvanized steel with a 0,3mm of thickness and 2 security clips with a 65mm of height and a width of 45mm with 0,3mm of thickness of the installation system.

The suspension system shall be manufactured from engineered ceiling thickness to support the full weight of the system including the safety ratio as determined by the local building and construction codes.

Method of attaching to the ceiling structure to be coordinated with the structural steel contractor or the structural contractor as appropriate.

Wood ceilings:

System shall incorporate:

- Flat surface formed by composite wood Fire Resistant (class A per ASTM E84) veneered in both faces whit a total thickness of 18mm

- The wood ceiling module is 610mm x 610mm or 610mm x 1220mm

- The wood ceiling shall comprise the following components:

  - 15/16” T-Grid profile system

  - Antiseismic clips

  - Security clips

    - Material quality and finishes:

  - Finishes can be perforated, unperforated or grooved.

  - Veneer Alternatives:

Specifier select finish from current selections, please proceed to: http://www.hunterdouglascontract.com/ceilings/woodwright/naturaplanktile/index.jsp

- EXECUTION

3.1   FABRICATION:

3.1.1	System components manufactured and assembled allowing for custom installation techniques to suit project requirements

3.1.2	Finished assemblies shall be square, true to size and free from twist or other defects that could affect their strength or appearance. Factory applied finish should be uniform, smooth and without blemishes

3.2   INSTALLATION:

3.2.1	Install work using skilled tradesman and install in strict accordance with manufacturer’s recommendations.

3.2.2	All items installed, plumbed, squared and rigidly anchored maintaining uniform clearances and accurate alignment measurements

3.2.3	The horizontal Wood ceiling shall be pre-measured and manufactured off-site

  - ADJUSTING AND CLEANING:

3.3.1	Adjust components as required to ensure trouble free performance

3.3.2	Prior to Substantial Completion clean down once the horizontal wood ceiling.

3.3.3	Replace work which cannot be satisfactorily repaired, adjusted or cleaned.

END